## Slide 1
IoT NETWORK ROUTING
A New Routing Objective Function for
IETF 6TiSCH Protocol
Burak Aydın, Sedat Görmüş, Hakan Aydın, Sercan Külcü
Computer Engineering Department, Karadeniz Technical University, Trabzon, Türkiye
30th IEEE Signal Processing and Communications Applications Conference (SIU 2022) | May 15-18, 2022, Safranbolu, Türkiye

## Slide 2
Introduction & Motivation
Industrial IoT (IIoT) demands high reliability against interference and multipath fading, plus predictable, low latency.
IEEE 802.15.4e / 6TiSCH combine TSCH scheduling with IPv6 to meet these needs in low-power, lossy networks.
RPL builds the routing topology, but its default Objective Functions cause frequent, costly parent switches — degrading reliability and increasing delay.
This study proposes a new parent-selection function that accounts for a node's neighbor count and traffic load to stabilize the network topology.
WHY IT MATTERS
21
nodes in the
simulated topology
2
new objective
functions proposed
50%
improvement in packet
delivery under weak links
2

## Slide 3
Background: RPL over 6TiSCH
RPL organizes the network as a Destination-Oriented Directed Acyclic Graph (DODAG), rooted at a sink node.
Each node computes a rank (distance from the root) and advertises routing metrics via DIO messages.
An Objective Function (OF) — e.g., MRHOF — defines how rank is computed and how the preferred parent is chosen.
6TiSCH allocates TSCH time-slot (cell) resources for each parent-child link — resources that must be fully reallocated on every parent switch.
Frequent or poorly chosen parent switches waste this allocation effort and cause packet loss and delay.
DODAG Formation
R
2
3
5
6
7
8
Root broadcasts DIO → nodes select a parent based on the Objective Function → tree topology emerges.
3

## Slide 4
The Problem: Unstable Parent Switching
Default RPL compares a candidate parent's rank to the current parent's rank using a fixed hysteresis threshold (MRHOF: 96 / 0.75 ETX; RFC 6719: 192 / 1.5 ETX).
A low, fixed threshold causes continuous parent switching — halting traffic, releasing and re-negotiating TSCH cells each time.
Switching cost is especially severe at critical relay nodes that serve many downstream nodes.
A relay node's parent switch forces traffic from all its dependents to buffer temporarily — risking buffer overflow and dropped packets.
Critical Relay Node Scenario
1
2
3
4
9
5
6
10
Node 4 (red) relays traffic for nodes 5, 6, 9, 10. If node 4 switches parent, all their traffic buffers temporarily — risking loss.
4

## Slide 5
Proposed Mechanism
Goal: optimize the parent-switching threshold using real-time node state, avoiding unnecessary resource-allocation cost.
Two new Objective Functions dynamically scale MRHOF's switching threshold:
SR1 — Neighbor-Count-Based
Scales the switching threshold by the node's neighbor count (bounded between 2 and 6 neighbors), making well-connected nodes more resistant to unnecessary switches.
SR2 — Cell-Count-Based
Scales the threshold by the number of allocated transmission cells, protecting nodes that already carry significant scheduled traffic.
If a node has no allocated transmission cell, the maximum link metric is added to its parent's cost — keeping it from being preferred until it establishes cells.
5

## Slide 6
Objective Function Logic
1
Check Cells
If a node has 0 allocated transmission cells, add the maximum link metric to its cost — deprioritize it.
→
2
Compute Threshold
Otherwise, scale the switching threshold by neighbor count (SR1) or cell count (SR2), bounded to avoid runaway values.
→
3
Compare Costs
Compare candidate parent cost against current parent cost ± the dynamic threshold.
→
4
Select Parent
Keep the current parent if within threshold; otherwise select the lower-cost candidate.
This logic runs at every RPL parent-comparison event, keeping well-connected or heavily-loaded relay nodes stable.
6

## Slide 7
Experimental Setup
Simulator
Cooja, on Contiki-NG
Topology
21 nodes (1 server + 20 client), Exp5438 modules, randomly placed
MAC Model
6TiSCH
Propagation
Cooja UDGM
Objective Functions
MRHOF (baseline), SR1, SR2 (proposed)
Rx Success Rate
70%, 80%, 90% (tested separately)
Transmission Range
50 m
Test Duration
1 hour, 5 repetitions per configuration, averaged
7

## Slide 8
Results: Delivery Rate & Parent Switches
Packet Delivery Ratio (%)
Chart: Network Rx Rate
| 70% | 80% | 90%
MRHOF | 43 | 60 | 70
SR1 | 50 | 61 | 68
SR2 | 46 | 53 | 70
Total Parent Switches
Chart: Network Rx Rate
| 70% | 80% | 90%
MRHOF | 480 | 340 | 55
SR1 | 65 | 55 | 45
SR2 | 265 | 150 | 60
Both SR1 and SR2 improve packet delivery over baseline MRHOF, especially at lower Rx rates (weaker links) — and dramatically reduce parent-switch counts, most notably SR1.
8

## Slide 9
Results: Latency & Discussion
Chart: Avg. Delay per Packet (ms)
| 70% | 80% | 90%
MRHOF | 190 | 155 | 95
SR1 | 128 | 128 | 92
SR2 | 128 | 128 | 90
1
Up to 50% Faster Delivery
Under weak-link conditions (low Rx rate), SR1/SR2 reduce delay by up to 50% versus MRHOF.
2
Fewer Buffer Overflows
Fewer parent switches mean fewer packets stuck in limited node buffers awaiting new-parent cell allocation.
3
Trade-off Is Minimal
Gains in stability and delivery come at negligible cost to rank-computation complexity.
9

## Slide 10
Conclusion
Two new Objective Functions (SR1, SR2) dynamically scale RPL's parent-switching threshold using neighbor count or allocated-cell count.
Both significantly reduce unnecessary parent switches versus standard MRHOF — SR1 shows the strongest stability gains.
Packet delivery time improves by up to 50% under weak-link conditions, where stability matters most.
Future work: enhance these objective functions with reinforcement-learning-based approaches for adaptive, data-driven parent selection.
50%
Faster packet delivery
under weak links
21 nodes
simulated topology
2 new
objective functions
Contact: sercan.kulcu@ceng.ktu.edu.tr
10