## Slide 1
RESEARCH ARTICLE · TURKISH JOURNAL OF ELECTRICAL ENGINEERING & COMPUTER SCIENCES · 2019
Enabling Space Time Division
Multiple Access in IETF 6TiSCH Protocol
Using directional antennas to schedule resources in time, frequency, and space
Sedat Görmüş · Sercan Külcü
Department of Computer Engineering, Faculty of Engineering, Karadeniz Technical University, Trabzon
Turk J Elec Eng & Comp Sci (2019) 27: 4151–4166 · doi:10.3906/elk-1903-127

## Slide 2
SUMMARY
What Problem Does This Study Solve?
1
The Problem
6TiSCH networks don't perform as expected when frequency resources are limited and the same band is shared with WiFi, Bluetooth, and other technologies.
2
The Approach
A simple, switchable directional antenna system is integrated with the IETF 6TiSCH protocol.
3
What's New
Resources are scheduled not only in time and frequency, but also in space (direction) — an algorithm called SF-DA.
4
The Finding
In Cooja/Contiki simulations, packet delivery goes up clearly, while delay and energy use drop significantly.
Görmüş, Külcü (2019)
2

## Slide 3
1 · INTRODUCTION
Why Do We Need Directional Antennas?
The challenge facing IoT networks
New applications — smart grids, smart health, smart cities — are quickly increasing the need to connect small devices to the Internet.
As cell sizes shrink, nodes using the same or nearby frequency channels interfere with each other more often.
Omnidirectional antennas broadcast in every direction, so they limit how well the wireless space can be reused.
A solution: low-cost radios with sectorized or directional antennas that enable space division multiple access (SDMA).
4
IEEE 802.15.4 channels that
don't overlap with WiFi (15, 20, 25, 26)
2–3
Directional antennas
tested in this study
25–101
Different network sizes
used in the tests
Source: Soua & Minet (2015); Görmüş & Külcü (2019), Section 1
3

## Slide 4
1.1 · CONCEPT
Omnidirectional vs. Directional Antennas
📡
Omnidirectional
Sends energy equally in all directions
Low reuse of the wireless space
Higher risk of co-channel interference and collisions
Needs more power to reach the same distance
🧭
Directional
Focuses energy toward one direction
High reuse of the wireless space
Fewer collisions and less interference
Needs less power to reach the same distance
Source: Wong et al. (2015); Dai et al. (2013)
4

## Slide 5
2 · BACKGROUND
The IETF 6TiSCH Protocol Stack
Application / CoAP / PCE / Tracking
TCP/UDP/IPv6 + RPL
Routing
6LoWPAN
IPv6 over the 802.15.4 physical layer
6Top
Distributed scheduler — shares cells between pairs of nodes
802.15.4e TSCH MAC
Collision-free access using time slots and channel hopping
IEEE 802.15.4 (Physical Layer)
Source: Figure 1b, p.4154 (Görmüş & Külcü 2019)
5

## Slide 6
CONTRIBUTION
The Main Contribution of This Study
🧭
Direction-aware scheduling
A directional-antenna-aware resource scheduling mechanism (SF-DA) is proposed for 6TiSCH networks.
🔀
A hybrid access scheme
Resources are shared across three dimensions: time, frequency, AND space (direction).
💻
Cooja / Contiki integration
A switchable directional antenna model was added as a new module to Contiki OS's Cooja simulator.
📊
A fair comparison
The proposed solution is compared against the 6TiSCH Minimal Configuration and Orchestra scheduling mechanisms.
6

## Slide 7
3 · SYSTEM MODEL
A Multi-Antenna Architecture for Cooja
How was it built?
The TI EXP430F5438 platform was extended with 2–3 CC2420 radio interfaces, each facing a different direction.
Each interface connects to Cooja through its own SPI port on the Contiki cc2420 driver.
The UDGM radio medium was updated to also take transmission direction into account.
The direction of an incoming packet is stored in the MAC layer's neighbour table.
Contiki (Emulation)
Cooja (Simulation)
CC2420
Driver
Exp5438
Node
UDGM
Radio Medium
SPI Bus
→
→
CC2420 class
CC2420 class
CC2420 class
All 3 directional antenna interfaces are simulated in the same radio medium
Source: Figure 2, p.4156 (Görmüş & Külcü 2019)
7

## Slide 8
4 · METHOD
Space-Time Scheduling: A Worked Example
In a 9-node mesh network, every node sends 1 packet to the root node. Compare how many time slots are needed to carry the same traffic:
Omnidirectional Antenna
10
time slots needed
Nodes cannot communicate at the same time; transmissions must happen one after another.
Directional Antenna (SF-DA)
8
time slots are enough
Space-time separation allows more transmissions to happen in parallel.
Source: Figure 3, p.4158 (Görmüş & Külcü 2019)
8

## Slide 9
5 · TEST SETUP
Test Environment and Parameters
MAC Parameters
Min. back-off exponent | 1
Max. back-off exponent | 7
Back-off increment | 2
Retransmission count | 5
Frame / Timing Parameters
Frame size | 127 bytes
Buffer depth | 5
Timeslot duration | 15 ms
Slotframe length | 15
Network Parameters
Transmit range | 50 m
Interference range | 100 m
Node distance | 40 m
Test duration | 2 hours
A 25-node grid topology (200×150 m) was tested with 2 or 3 directional antennas, using 180° / 120° beam widths.
Source: Table 1, p.4160
9

## Slide 10
6 · RESULTS
PRR Performance: Minimal Configuration and Orchestra
📶
Minimal Configuration
Using directional antennas increases the average packet reception ratio (PRR) by 2 to 3 times, depending on the data rate.
🎼
Orchestra Scheduling
A similar improvement is seen here too — directional antennas clearly boost network performance under heavy load.
📡
Why does this happen?
A narrow antenna beam width gives higher spatial separation, which reduces collisions in shared time slots.
Test setup: the packet transmission interval was varied between 0.2 and 2 packets/second to create saturated traffic scenarios.
Source: Figure 4, p.4161 (Sections 5.1–5.2)
10

## Slide 11
6 · RESULTS
Space-Time Scheduling: Collisions and Channel Count
↑100%
The largest PRR improvement seen in the evaluated scenario
>8
Above this number of channels, directional antennas add little benefit
50%
How much less transmit power a 180° directional antenna needs for the same range
Key takeaways
When there are only a few frequency channels, the extra spatial dimension from directional antennas clearly improves PRR.
In networks with low interference and few nodes, directional antennas may add only a limited benefit.
SF-DA performance improves as more antennas are added; the benefit becomes even clearer as channel quality gets worse.
Source: Figures 5–6, p.4162 (Section 5.3)
11

## Slide 12
6 · RESULTS
Delay, Energy Use, and Network Size
As the network gets bigger, PRR drops while delay and energy use go up. Compared to an omnidirectional antenna, using 3 directional antennas gives:
+5–10% higher PRR
−50% lower average network delay
↓ Energy use, clearly reduced
 | 1 directional antenna |  |  | 2 directional antennas |  |  | 3 directional antennas |  | 
Number of Nodes | PRR % | Delay (ms) | Energy (mWh) | PRR % | Delay (ms) | Energy (mWh) | PRR % | Delay (ms) | Energy (mWh)
25 | 94.87 | 1267 | 3.21 | 97.94 | 595 | 1.55 | 100 | 536 | 1.26
49 | 83.55 | 1560 | 3.65 | 87.61 | 1174 | 1.82 | 88.77 | 1094 | 1.49
73 | 61.04 | 2254 | 4.09 | 63.49 | 1594 | 1.89 | 66.74 | 1544 | 1.65
101 | 39.13 | 3145 | 5.08 | 42.17 | 2324 | 2.31 | 44.06 | 1793 | 1.77
Source: Table 2, p.4164
12

## Slide 13
CONCLUSION
Directional Antennas Add a New Degree of Freedom
Using a simple, RF-switchable smart antenna system improves 6TiSCH network performance and reduces end-to-end delay and energy use.
6TiSCH performance improves clearly when scheduling decisions use the direction information gathered by the smart antennas.
The benefit of directional antennas is greatest in scenarios where the number of frequency channels is limited.
Future work: validate these results using a testbed with real switchable and steerable antennas, aiming at high-reliability industrial IoT networks.
13

## Slide 14
REFERENCE
Source and Acknowledgment
Görmüş, S., Külcü, S. (2019).
Enabling space time division multiple access in IETF 6TiSCH protocol.
Turkish Journal of Electrical Engineering and Computer Sciences, 27(6), 4151–4166. doi:10.3906/elk-1903-127
This research was supported by the Scientific and Technological Research Council of Turkey (TÜBİTAK), project number 118E289.
This presentation is an academic summary of the research paper above. For the full reference list (29 citations), please see the original article.
Thank You
14