## Slide 1
RESEARCH ARTICLE · SENSORS (MDPI), VOL. 26 · 2026
High-Precision Marine Radar Object Detection
Using Tiled Training and SAHI Enhanced
YOLOv11-OBB
Finding small ships on radar screens with over 95% precision
Sercan Külcü
Computer Engineering Department, Giresun University, Turkey
Sensors 2026, 26, 942 · doi:10.3390/s26030942

## Slide 2
SUMMARY
What Did This Study Find?
1
Main Finding
Tiled training + SAHI + YOLOv11-OBB reaches over 0.95 mAP@0.5 on real radar data — beating standard full-image detection.
2
Why OBBs Help
Oriented bounding boxes (OBBs) fit ships more tightly than ordinary boxes or masks, since they follow the ship's true heading.
3
Practical Payoff
The pipeline is lightweight enough to run in near real time on edge hardware — suitable for small and medium-sized vessels.
4
Maritime Impact
Accurate orientation and centre-point estimates support better multi-target tracking and collision avoidance.
Külcü (2026)
2

## Slide 3
1 · MOTIVATION
Why Is Marine Radar Detection So Hard?
The core challenge
Radar screens are full of sea clutter, small distant targets, and fixed navigation markers that look like ships.
Classic methods (like CFAR statistical detectors) work, but struggle when clutter changes quickly or targets are faint.
Recent deep learning models (YOLO-based, GAN-based, multi-sensor fusion) do better, but most still use plain, axis-aligned boxes.
A key gap remains: resizing large radar images to fit standard network inputs (e.g. 640×640) makes small ships disappear.
What earlier studies achieved
CFAR + superpixels
84.8% detection rate
Marine-Faster R-CNN
93.65% recall
YOLO-SWFormer
91.8% recall
YOSMR (lightweight)
93.1% recall, 92.0% accuracy
Radar + camera fusion
88.6% mAP@0.5
None of these combine tiled training + slicing + orientation-aware boxes — the gap this paper fills.
Source: Section 1 (Külcü 2026)
3

## Slide 4
CONTRIBUTION
Four Contributions to the Field
🧩
Tiled + SAHI + OBB pipeline
A combined pipeline that fixes the resolution mismatch in large radar images, greatly improving small-target detection.
🧭
Orientation-aware detection
OBBs model the true heading of each vessel, cutting false positives from clutter and fixed navigation aids.
🏷️
Semi-automatic annotation
A contour-based labelling method builds three label types — box, oriented box, and mask — straight from raw radar echoes.
🏆
New performance benchmark
Over 0.95 mAP@0.5 and sub-10-pixel localization error, while staying fast enough for edge devices.
4

## Slide 5
2.1 · DATASET
The DAAN Marine Radar Dataset
Collected by the German Aerospace Center (DLR) in the Baltic Sea
X-band radar mounted on a moving "own-ship", using standard nautical PPI mode at a 3 nautical-mile range.
4 target vessels, tracked for about 13 minutes, with very different speeds, headings, and crossing/overtaking manoeuvres.
Frames also contain wake trails, sea clutter, and interference from fixed navigation aids.
AIS data (real GPS-based ship positions) is used as accurate ground truth for evaluating detections.
760
full-resolution radar frames
4
vessels tracked, plus the moving own-ship
1 Hz
frame capture rate, ~13 minutes total
Source: Section 2.1, Figs. 1–2 (Külcü 2026)
5

## Slide 6
2.2 · METHOD
Turning Raw Echoes into Training Labels
1. Find Candidates
Convert the image to HSV colour space and threshold the bright yellow used for strong echoes.
→
2. Build Labels
For each surviving shape, compute a box, an oriented box, and a smoothed outline (mask) at the same time.
→
3. Human Check
About 15% of frames needed a manual fix — splitting merged ships, joining broken echoes, or removing false navigation-aid shapes.
Only ~15% of frames needed manual correction — because the radar display uses a fixed colour code for strong echoes, automatic thresholding worked well for most frames. This check happens only once, offline; the trained model runs fully automatically afterwards.
Source: Section 2.2 (Külcü 2026)
6

## Slide 7
2.2 · LABELS
Three Label Formats, One Contour
Axis-Aligned Box
The smallest upright rectangle around the shape. Simple, but loose-fitting for tilted ships.
Oriented Box (OBB)
The smallest rotated rectangle. Matches the ship's real heading for a tight, accurate fit.
Segmentation Mask
A smoothed polygon outline (Douglas–Peucker algorithm), capturing the exact silhouette.
Yellow-echo threshold (HSV)
hue ∈ [20°, 40°], saturation ∈ [100, 255], value ∈ [100, 255]
Shapes smaller than 8 pixels are dropped as noise.
Mask smoothing precision
ε = 0.01 × perimeter
Keeps the outline's shape while removing extra, redundant points.
Source: Section 2.2.1–2.2.2, Eq. (1)–(2), Algorithm 1 (Külcü 2026)
7

## Slide 8
2.4 · METHOD
Tiled Training: Keeping Small Ships Visible
Resizing a large radar image down to 640×640 pixels makes small, distant ships shrink to almost nothing. The fix: cut each image into overlapping tiles first.
640×640 px
size of each tile
(20% overlap, 512 px steps)
760 → 3,040
training images
after tiling (4× more)
4,457 → 11,893
labelled ship instances
available for training
Only tiles that contain at least one ship are kept — this avoids wasting training time on empty sea. Labels are automatically re-calculated for each tile's own coordinate space.
Source: Section 2.4.2 (Külcü 2026)
8

## Slide 9
2.3, 2.5 · MODELS
Three YOLOv11 Variants, Enhanced with SAHI
▭
YOLOv11-detect
Standard detection with axis-aligned boxes (center, width, height).
◈
YOLOv11-obb
Predicts a rotated box using four corner points — matches vessel heading.
◐
YOLOv11-seg
Adds pixel-level masks for the exact shape of each echo.
🔍 SAHI — Slicing Aided Hyper Inference
At test time, SAHI cuts each full-resolution radar image into overlapping 640×640 slices, runs the model on each slice separately, and merges the results back together. This matches the resolution the model was trained on — without ever retraining it.
Source: Sections 2.3, 2.5 (Külcü 2026)
9

## Slide 10
3.1 · RESULTS
Choosing a Backbone: Lightweight YOLO Comparison
Model | Parameters | GFLOPs | mAP@0.5 | mAP@0.5:0.95 | Inference (ms)
YOLOv5n | 2.5 M | 7.1 | 0.981 | 0.787 | 2.7
YOLOv8n | 3.0 M | 8.1 | 0.987 | 0.797 | 2.7
YOLO11n | 2.6 M | 6.3 | 0.984 | 0.816 | 2.9
YOLO26n | 2.4 M | 5.2 | 0.987 | 0.807 | 2.8
Source: Table 1, Section 3.1 (Külcü 2026)
10
All variants score above 0.98 mAP@0.5. YOLO11n was chosen: it gives the best mAP@0.5:0.95 (0.816) — the strictest, most demanding accuracy measure.

## Slide 11
3.2 · RESULTS
Full-Image Resizing vs. Tiled Training
Model | Training Method | mAP@0.5 | mAP@0.5:0.95
YOLOv11-detect | Resized | 0.921 | 0.681
YOLOv11-detect | Tiled | 0.984 | 0.816
YOLOv11-obb | Resized | 0.955 | 0.799
YOLOv11-obb | Tiled | 0.989 | 0.882
YOLOv11-seg | Resized | 0.922 | 0.668
YOLOv11-seg | Tiled | 0.985 | 0.810
Source: Table 2, Section 3.2 (Külcü 2026)
11
Tiled YOLOv11-OBB wins overall: 0.989 mAP@0.5 — the highest score in the study, and a clear jump over its resized counterpart (0.955).

## Slide 12
3.3 · RESULTS
Tuning SAHI: Overlap Ratio and Slice Size
Overlap ratio (0.1 → 0.5)
Overlap | mAP@0.5 | mAP@0.5:0.95 | mAP@0.75
0.1 | 0.962 | 0.487 | 0.380
0.2 | 0.962 | 0.488 | 0.381
0.4 | 0.961 | 0.489 | 0.392
0.5 | 0.962 | 0.490 | 0.394
Slice size (640 px → 240 px, overlap fixed at 0.2)
Slice | mAP@0.5 | mAP@0.5:0.95 | mAP@0.75
640 px | 0.962 | 0.488 | 0.381
512 px | 0.973 | 0.506 | 0.426
448 px | 0.971 | 0.509 | 0.447
320 px | 0.977 | 0.512 | 0.486
240 px | 0.976 | 0.501 | 0.459
Key takeaways
A bigger overlap gives a small, steady gain — useful when precision matters more than speed.
Shrinking the slice size helps a lot — mAP@0.75 nearly doubles (0.381 → 0.486) — but going too small (240 px) starts to hurt, since there are too many boundary artifacts.
320 px slices give the best accuracy; 640 px with 0.2 overlap is the best speed/accuracy balance.
Source: Tables 3–4, Section 3.3 (Külcü 2026)
12

## Slide 13
3.3 · RESULTS
Comparing Variants: Accuracy vs. Precision/Recall
mAP at different strictness levels
Model | mAP@0.5 | mAP@0.5:0.95 | mAP@0.75
Detect | 0.962 | 0.488 | 0.381
OBB | 0.954 | 0.374 | 0.428
Segment | 0.948 | 0.494 | 0.441
Precision & Recall at IoU = 0.5
Model | Precision | Recall
Detect | 0.929 | 0.958
OBB | 0.912 | 0.955
Segment | 0.873 | 0.955
How to read this: the plain detect model has the best raw precision and recall — but its accuracy drops fastest at strict thresholds (mAP@0.75 = 0.381). OBB and Segment keep much more of their accuracy at mAP@0.75 (0.428 and 0.441), proving that they draw tighter, more reliable boundaries around each ship — even if they occasionally flag a few more false positives.
Source: Tables 5–6, Section 3.3 (Külcü 2026)
13

## Slide 14
3.4 · RESULTS
How Close Are Predictions to the Real Ship Position?
Mean distance (in pixels) between the predicted centre point and the true AIS-based position:
Vessel | Model | Mean (px) | Median (px) | Std. Dev. (px)
Vessel 2 | Detect | 6.33 | 6.05 | 3.10
Vessel 2 | OBB | 6.30 | 6.00 | 3.04
Vessel 2 | Segment | 6.75 | 6.30 | 2.98
Vessel 4 | Detect | 5.14 | 5.20 | 2.99
Vessel 4 | OBB | 5.06 | 5.10 | 3.10
Vessel 4 | Segment | 5.62 | 5.45 | 2.93
All three models stay under 10 pixels of mean error — and OBB is consistently the most accurate at finding a ship's true centre, confirming that orientation-aware boxes track vessels more faithfully.
Source: Table 7, Section 3.4 (Külcü 2026)
14

## Slide 15
3.5–3.7 · PRACTICAL VIEW
Speed on Real Hardware, and When It Fails
Computational efficiency
Model size
~5.5–6.0 MB
Peak memory use
< 4.2 GB
Full-image inference
18–22 FPS
Tiled + SAHI inference
4–6 FPS
4–6 FPS is a 3–4× slowdown versus full-image inference — but still enough for near-real-time collision avoidance and AIS-linked tracking.
Six typical failure patterns
• Weak echo from signal attenuation → missed target
• Wave clutter hides the vessel's signature
• Slicing (SAHI) splits one ship's echo across two tiles
• Sharp manoeuvres change the echo shape too fast
• One ship's echo splits into two false detections
• Two nearby ships merge into a single, undercounted echo
Source: Sections 3.5, 3.7 (Külcü 2026)
15

## Slide 16
CONCLUSION
Scale-Aware and Orientation-Aware Design Wins
Combining tiled training, SAHI, and YOLOv11-OBB sets a new benchmark for marine radar detection: over 0.95 mAP@0.5 with sub-10-pixel localization error.
This solves two problems at once — the resolution mismatch that hides small ships, and the orientation blindness of ordinary bounding boxes.
The segmentation variant adds further value for tasks like separating overlapping wakes or tracking individual vessels.
Future work: speed up the pipeline (model pruning, lighter backbones), add sea-state labels to study weather effects, and test on more public radar datasets.
16

## Slide 17
REFERENCE
Source
Külcü, S. (2026).
High-Precision Marine Radar Object Detection Using Tiled Training and SAHI Enhanced YOLOv11-OBB.
Sensors, 26(3), 942. doi:10.3390/s26030942
Dataset: DAAN marine radar repository, German Aerospace Center (DLR) — https://doi.org/10.26090/rwmr
This presentation is an academic summary of the research paper above. For the full reference list (27 citations), please see the original article.
Thank You
17