## Slide 1
SMART ANTENNAS FOR IoT NETWORKS
Improving Synchronization Time in 6TiSCH
Networks with Smart Antennas
Sercan Külcü, Sedat Görmüş
Department of Computer Engineering, Karadeniz Technical University, Trabzon, Türkiye
30th IEEE Signal Processing and Communications Applications Conference (SIU 2022) | May 15-18, 2022, Safranbolu, Türkiye

## Slide 2
Introduction & Motivation
IETF 6TiSCH schedules time-slot and frequency-channel resources to build reliable, low-power, low-latency IoT networks.
Smart/directional antennas boost performance further — longer range and reduced interference by focusing energy in a chosen direction.
But narrow antenna coverage makes network synchronization and neighbor discovery much harder than with omnidirectional antennas.
This study proposes a new 6TiSCH message packet and mechanism letting nodes discover neighbors before full network synchronization.
WHY IT MATTERS
25–75
nodes tested across
density scenarios
~25%
faster sync with
scanning packets
2
antenna types compared:
omnidirectional vs. rotating
2

## Slide 3
Background
1
Smart / ESPAR Antennas
Electronically Steerable Parasitic Array Radiator antennas adjust radiation direction electronically, reducing interference and collisions in dense IoT deployments.
2
6TiSCH Protocol Stack
Uses Time-Slotted Channel Hopping (TSCH) for stable, low-power, low-latency medium access — achieving over 99% packet delivery in ideal conditions.
3
Two-Phase Network Formation
(1) Enhanced Beacon (EB) messages synchronize nodes to the network; (2) DIO messages build the routing tree (DODAG).
4
The Directional Antenna Challenge
Narrow beam coverage means nodes must repeat neighbor-discovery steps across many directions — far slower than with omnidirectional antennas.
3

## Slide 4
Modeling the Antenna Radiation Pattern
Cooja's radio model was extended to account for each node's antenna orientation, not just inter-node distance.
+5 dBi gain in the antenna's facing direction; −15 dBi loss in the opposite direction.
Result: ~30 m range in the facing direction vs. ~40 m of interference protection from unwanted directions.
Signal strength (RSS) follows a log-distance path-loss model incorporating inter-node distance and relative antenna angles:
RSS = P_TX + P_PL − 10K·log₁₀(d₁₂ / d₀) + G(θ₁₂) + G(θ₂₁)
Modeled Radiation Pattern
Main lobe: +5 dBi
Back lobe: −15 dBi
Directional gain trades 360° coverage for extended range and interference rejection.
4

## Slide 5
Proposed Mechanism: Scanning Packets
1
Broadcast Scanning Packet
Unsynchronized nodes broadcast a new "Scanning Packet" while their radio stays open, listening across frequencies.
→
2
Extract Neighbor Info
Receiving nodes extract the sender's MAC ID, current antenna angle, and RSSI to build a virtual neighbor list (Algorithm 1).
→
3
Synchronize via EB
Once a node receives an Enhanced Beacon (EB) and synchronizes, it stops sending scanning packets and starts sending EB itself.
→
4
Directed Transmission
Future broadcasts on shared cells target a known neighbor's direction (Algorithm 2) instead of a random direction — raising success rate.
New nodes can still be discovered: when transmitting or listening, a random direction is chosen with probability P = 1 / (neighbor count + 1).
5

## Slide 6
Experimental Setup
Simulator
Cooja, on Contiki OS — 10 repetitions, averaged
Frame Length
101 slots
Shared Cells
1
EB Send Interval
16 s (min) – 50 s (max)
Range (Omnidirectional)
50 m
Range (Smart Antenna)
15 – 80 m
Scenario Area
200 m × 200 m
Node Count Tested
25, 35, 45, 55, 65, 75
Test runs until the network is fully synchronized. Nodes are placed randomly within the scenario area.
6

## Slide 7
Results: Sync Time by Antenna Configuration
Chart: Node Count
| 25 | 35 | 45 | 55 | 65 | 75
Rotating antenna | 3.2 | 3 | 3.8 | 5.5 | 9 | 16.5
Rotating + Scanning packet | 2 | 2 | 2.3 | 3 | 4 | 5.5
Rotating + Autonomous cell | 1.5 | 1.5 | 1.6 | 1.8 | 2 | 2.2
Omnidirectional | 1.8 | 2.2 | 3.5 | 6.5 | 11 | 18
Omnidirectional + Autonomous cell | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8
Autonomous-cell solutions scale best as density increases; scanning packets help rotating antennas the most in dense scenarios.
7

## Slide 8
Results: Effect of Scanning Packets
Chart: Node Count
| 25 | 35 | 45 | 55 | 65 | 75
Random direction (1 freq.) | 8 | 10 | 15 | 22 | 32 | 42
Random direction (2 freq.) | 12 | 15 | 20 | 28 | 38 | 47
Scanning packet (1 freq.) | 3 | 3.5 | 5 | 8 | 12 | 17
Scanning packet (2 freq.) | 5 | 6 | 8 | 12 | 16 | 20
~25%
Faster network synchronization using scanning packets vs. random-direction transmission.
More frequency channels increase total sync time (each must be scanned in turn) — but scanning packets consistently outperform random-direction transmission at every channel count.
8

## Slide 9
Discussion
1
Omnidirectional Struggles at Scale
Performs well in small scenarios, but degrades sharply as density rises due to more frequent interference and collisions.
2
Rotating Antennas Excel in Dense Networks
Narrow beams reduce collisions as density increases — but need more neighbors in range before showing this benefit.
3
Autonomous Cells Are the Biggest Win
Duplicating control messages per neighbor and sending over dedicated, autonomously assigned cells keeps sync time short and scalable, regardless of density.
4
Scanning Packets Complement Autonomous Cells
By directing shared-cell transmissions toward known neighbors instead of random directions, sync time improves by up to 25%.
9

## Slide 10
Conclusion
A new Scanning Packet lets unsynchronized nodes with directional antennas discover neighbors faster in 6TiSCH networks.
Directing shared-cell transmissions toward known neighbors — rather than random directions — improves synchronization time by ~25%.
Autonomously assigned cells per neighbor provide the largest, most scalable improvement across all tested node densities.
Future work: apply machine-learning approaches to further optimize shared-cell utilization in directional 6TiSCH networks.
~25%
Faster network
synchronization
25–75 nodes
tested densities
New Scanning
Packet mechanism
Contact: sercan.kulcu@ceng.ktu.edu.tr | Supported by TÜBİTAK Project No. 118E289
10