## Slide 1
RESEARCH ARTICLE · IEEE ACCESS, VOLUME 9 · 2021
Integration of Steerable Smart Antennas
to IETF 6TiSCH Protocol for High Reliability
Wireless IoT Networks
A smart antenna solution that helps 6TiSCH networks stay reliable as they grow
Sercan Kulcu · Sedat Gormus · Yichao Jin
Department of Computer Engineering, Karadeniz Technical University, Trabzon, Turkey
Bristol Research and Innovation Laboratory, Toshiba Europe Ltd., Bristol, U.K.
IEEE Access, vol. 9, pp. 147780–147790, 2021 · doi:10.1109/ACCESS.2021.3125144

## Slide 2
SUMMARY
What Problem Does This Paper Solve?
1
The Problem
Steerable smart antennas need complex algorithms, which are hard to use in low-power, low-cost IoT devices.
2
The Approach
The paper adds a low-complexity steerable antenna solution to the IETF 6TiSCH protocol, called SAA6.
3
What's New
New MAC-layer and scheduling mechanisms let nodes find and track the best antenna direction on their own.
4
The Finding
In Cooja/Contiki simulations, SAA6 beats the standard omnidirectional 6TiSCH stack, especially in dense networks.
Kulcu, Gormus, Jin (2021)
2

## Slide 3
1 · INTRODUCTION
Why Combine Steerable Antennas with 6TiSCH?
The challenge
IoT networks often use many low-cost nodes that send data at the same time, which causes interference and dropped packets.
This problem gets worse in dense networks, where bandwidth is limited and channels are shared with WiFi and other technologies.
Directional antennas can reduce interference, but using them well requires new, carefully designed protocols.
This paper builds those mechanisms directly into 6TiSCH, the leading protocol for reliable industrial IoT.
8
Maximum number of neighbours
stored per node
5 dBi
Maximum gain of the
modelled steerable antenna
81
Nodes in the largest
test network
Source: Section I (Kulcu et al. 2021)
3

## Slide 4
2 · BACKGROUND
Smart Antennas: Two Main Types
🔀
Switched Beam
Has several fixed beam patterns
Can act like an omnidirectional antenna when broadcasting
Simple to control, but less flexible
🎯
Adaptive Array
Can steer its beam toward any direction
Can cancel signals coming from unwanted directions
Cannot transmit omnidirectionally
📡 ESPAR Antenna
An Electronically Steerable Parasitic Array Radiator (ESPAR) is a popular, easy-to-build option: one active element surrounded by passive elements. Changing the passive elements' values steers the beam electronically — with a full 360° scan, in steps as small as 30°, and gains of 7.5–9 dBi depending on the design.
Source: Section II-A (Kulcu et al. 2021)
4

## Slide 5
2 · BACKGROUND
6TiSCH in Brief: Two Cell Types
🔀
Shared Cell
Uses slotted-ALOHA with contention. Nodes use it to send control frames (EB, RPL, DIS) and to negotiate new cells with neighbours.
🔒
Dedicated Cell
Reserved for one pair of nodes. Gives interference-free, collision-free communication for high reliability.
How a node joins the network
1. Get synchronized — listen for Enhanced Beacon (EB) frames and learn the minimal schedule.
2. Join the routing tree — exchange RPL DIO frames to attach to a parent, forming a tree rooted at the sink.
3. Start communicating — the node now has what it needs to talk to the rest of the network.
Source: Section II-B (Kulcu et al. 2021)
5

## Slide 6
CONTRIBUTION
SAA6: Steerable Antenna Agnostic 6TiSCH Solution
🧭
Faster neighbour discovery
A new, fully autonomous scheduling mechanism that finds neighbours faster, using a steerable antenna.
📶
RSSI-based direction finding
An algorithm that uses signal strength (RSSI) to work out the best transmit and receive direction, cutting interference.
🔀
Fewer shared-cell collisions
A method that uses directional communication to reduce collisions in shared cells — key for scaling up 6TiSCH networks.
6

## Slide 7
3 · ANTENNA MODEL
Modelling a Steerable Antenna
How the model works
Maximum antenna gain is set to 5 dBi, matching real ESPAR designs from the literature.
The receiver's gain depends on the angle θ between the transmitter's and receiver's antenna directions.
This gain is added directly into the standard path-loss (signal strength) formula.
Receiver sensitivity is set to −95 dBm, matching the CC2420 radio used in the test hardware.
G(θ) [dB] = 10(1 + cos θ) − 15
Antenna gain as a function of angle θ
+30 m
extra range at 0°
(main beam direction)
−40 m
shorter range at 180°
(opposite direction)
Reference distance: 1 m · Reference path loss: −52 dBm · Path-loss exponent: 2.5
Source: Section III, Eq. (1)–(2), Fig. 1 (Kulcu et al. 2021)
7

## Slide 8
4 · METHOD
Finding the Best Direction to Each Neighbour
How each node learns the best direction
Every node keeps a list of neighbours, storing each one's ID, best known direction, and the highest RSSI seen so far.
Each time a frame arrives successfully, the node compares the new RSSI with the stored value — if it's better, it updates the direction.
No extra "probing" frames are needed — normal control traffic (EB, RPL, DATA) is enough to learn the best direction.
Because antennas start out pointing randomly, this discovery process naturally takes longer than with omnidirectional antennas.
Result: RSSI improves over time
In a 40 m grid test network, RSSI values converge toward −82 dBm as node pairs gradually find their best antenna orientation.
Neighbour list size is capped at 8 neighbours per node to keep memory and processing needs low.
A frame update is skipped if a neighbour hasn't sent anything recently, saving energy.
Source: Section IV-A, Algorithm 1, Fig. 3 (Kulcu et al. 2021)
8

## Slide 9
4 · METHOD
Two Slotframes: One for Data, One for Control
The proposed solution runs two independent slotframes with lengths that are mutually prime, so they rarely overlap:
📦
Data Slotframe (SF0)
Scheduled by the standard 6TiSCH Scheduling Function Zero. Carries regular data traffic between nodes.
🔁
Autonomous Slotframe
Runs without any negotiation. Each node hashes its own ID and its neighbour's ID to pick a time slot and channel automatically.
Why two slotframes?
A directional antenna cannot broadcast to every neighbour at once — so multicast control messages need their own dedicated cells, sent one direction at a time.
Each node autonomously reserves 1 transmit and 1 receive cell per neighbour, moving this traffic off the contention-based shared cell.
Source: Section IV-C–D, Eq. (3), Fig. 4 (Kulcu et al. 2021)
9

## Slide 10
4.E · COST ANALYSIS
Is the Extra Signalling Worth It?
The autonomous cells add some overhead, but steerable antennas also need fewer hops to reach the root — so the net cost depends on the traffic rate:
Transmission Interval | Omnidirectional Cells | Steerable Cells | Ratio (Steerable / Omni)
1 s | 296 | 240 + 80 = 320 | 1.08
0.5 s | 592 | 480 + 80 = 560 | 0.94
+8%
more cells needed than omni, at a 1 s interval
−6%
fewer cells needed than omni, at a 0.5 s interval
~25%
fewer cells overall thanks to reduced hop count
Source: Table 1, Section IV-E, Eq. (4)–(8) (Kulcu et al. 2021)
10

## Slide 11
5 · TEST SETUP
Simulation Setup and Assumptions
Slotframe & Timing
Slotframe length | 51
Autonomous slotframe length | 397
Timeslot duration | 15 ms
Test duration | 2 hours
Antenna Range
Transmit range (omni) | 50 m
Interference range (omni) | 100 m
Transmit range (steerable) | 15–80 m
Shared cells (omni / steerable) | 3 / 1
Network Layout
Inter-node distance | 40 m
Network dimensions | 320 × 320 m
Min / max EB period | 16 s / 50 s
Min / max DIO interval | 4.1 s / 1048.6 s
Key assumptions: nodes are static with one fixed-power (0 dBm) radio; each steerable node can scan the full 360°; the root node uses three switchable 120° antennas that can also emulate omnidirectional behaviour.
Source: Table 2, Section V-A (Kulcu et al. 2021)
11

## Slide 12
6 · RESULTS
Synchronization Time and Collision Rate
⏱️
Synchronization Latency
Sync time grows with network size for every antenna type. SAA6 is much faster than a plain steerable antenna, and close to the omnidirectional baseline, thanks to autonomous cells — at the cost of slightly more energy.
💥
Shared-Cell Collision Rate
Steerable antennas cut the collision probability by more than 20% in shared cells — with no need for extra tricks like adjusting the beacon interval.
Note: because all synchronized nodes share the same frequency channel in the shared cell, adding more channels does very little to reduce collisions — antenna direction matters far more.
Source: Fig. 6(a)–(b), Sections V-B–C (Kulcu et al. 2021)
12

## Slide 13
6 · RESULTS
Packet Delivery and Energy Savings
+30%
higher packet delivery ratio (PDR) than omnidirectional, across tested transmission intervals
↑ PDR
with limited channels — the antenna direction acts as a third scheduling dimension
−20%
lower energy consumption thanks to longer range and fewer retransmissions
Why does this happen?
Shorter transmission intervals create heavier traffic, so SAA6's spatial separation matters most exactly when the network needs it.
With few frequency channels available, nodes often reuse the same channel offset — directional antennas reduce the resulting interference.
Fewer dropped frames means fewer retransmissions, which is the main reason energy consumption drops.
Source: Fig. 6(c)–(e), Sections V-D–E (Kulcu et al. 2021)
13

## Slide 14
CONCLUSION
6TiSCH Is Ready for Smart, Directional Antennas
SAA6 outperforms the standard omnidirectional 6TiSCH stack in every tested aspect, especially reliability and network throughput.
The gains are largest in dense networks and in scenarios with limited frequency channels — exactly where industrial IoT networks struggle most.
This confirms that 6TiSCH can support directional and smart antennas without losing its low-power, reliable design goals.
Future work: validate the results on real hardware, use machine learning to find the best antenna direction, and add multi-path communication to further cut network latency.
14

## Slide 15
REFERENCE
Source and Acknowledgment
Kulcu, S., Gormus, S., Jin, Y. (2021).
Integration of Steerable Smart Antennas to IETF 6TiSCH Protocol for High Reliability Wireless IoT Networks.
IEEE Access, 9, 147780–147790. doi:10.1109/ACCESS.2021.3125144
This research was supported by the Scientific and Technological Research Council of Turkey (TÜBİTAK), project number 118E289.
This presentation is an academic summary of the research paper above. For the full reference list (30 citations), please see the original article.
Thank You
15