## Slide 1
RESEARCH ARTICLE · SCIENTIFIC REPORTS
Overcoming Resolution Constraints in
Automated Colony Counting via SAHI
A high-performance tiled-inference deep learning framework that preserves native image resolution for accurate, lightweight bacterial colony detection
Sercan Külcü & Duygu Balpetek Külcü
Giresun University — Computer Engineering & Food Engineering
Scientific Reports (2026) 16:24516 | DOI: 10.1038/s41598-026-55724-1

## Slide 2
OVERVIEW
The Study at a Glance
Downscaling high-resolution Petri dish images to 640×640 pixels severely hurts lightweight detectors. This study shows that SAHI-based tiled inference — not bigger models — is the key to accurate, real-time bacterial colony counting.
96.9%
mAP@0.5 with
tiled YOLOv11n
2.6M
Parameters —
nano-scale model
<320 ms
Whole-plate
inference (RTX 3050)
23/24
Classes with
≥95% accuracy
KEYWORDS
Bacterial colony counting
Tiled inference
Small object detection
High-resolution imaging
SAHI
Lightweight YOLO models
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
2

## Slide 3
1. INTRODUCTION
Where Resolution Gets Lost
Clinical microbiology labs face growing sample volumes and need rapid, accurate colony detection. But standard detectors resize full Petri dish photographs down to a fixed input size — and that resizing quietly destroys the fine detail small, densely packed colonies depend on.
⊡
Downsampling destroys detail
Resizing a high-resolution plate to 640×640 pixels removes the fine spatial cues that separate tiny, tightly clustered colonies.
▦
Dense, real-world plates
Colony density ranges from under 10 to over 1,100 per plate — with some species growing in especially crowded patterns.
⚙
Laboratory hardware limits
Routine diagnostic labs need lightweight, nano-scale models that still run fast on consumer-grade GPUs.
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
3

## Slide 4
1. INTRODUCTION
Three Contributions
This study shows that resolution-preserving tiling — not model scaling — is the decisive factor for dense micro-colony detection.
1
Tiling beats resizing and architecture upgrades
Simple fixed-size tiled inference with moderate overlap clearly outperforms conventional resizing — and outperforms recent YOLO architectural advances.
2
High accuracy from lightweight nano-scale models
State-of-the-art detection accuracy is achievable with YOLOv11n at only 2.6M parameters, on consumer-grade hardware, with subsecond whole-plate inference.
3
A reproducible, lightweight pipeline
Avoids heavy backbones, multi-scale training, test-time augmentation, and ensembling — lowering barriers to adoption in clinical and veterinary microbiology.
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
4

## Slide 5
2. MATERIALS & METHODS
A Real-World Bacterial Colony Dataset
DATASET SUMMARY
369 Petri dish images captured with three different smartphones under real-world laboratory conditions — natural variation in lighting, reflections, background, and condensation.
56,865
Individually annotated colonies
24
Bacterial species (11 Gram+ / 13 Gram−)
≤1,100+
Colonies on the densest single plate
SPLIT & PREPROCESSING STRATEGY
Image-level split
80% dev / 20% independent test
Dev subsplit
80:20 → ~64% train / 16% val
Tile size
640 × 640 px, 20% overlap
Tiled dataset
9,220 labeled tiles (~25× more)
Media used
Blood, chocolate, nutrient, MacConkey agar
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
5

## Slide 6
2.1 SAHI-BASED TILED INFERENCE
Slicing the Plate to Preserve Detail
◎
Full-Res Plate
Original high-resolution
Petri dish photograph
→
▦
Overlapping Tiles
Sliced into 640×640 px
patches, 20% overlap
→
◉
Per-Tile Detection
YOLO nano model runs
independently on each tile
→
⌗
Merge + NMS
Coordinates remapped,
duplicates removed
SAHI (Slicing Aided Hyper Inference) is model-agnostic — it plugs into YOLOv5n, YOLOv8n, or YOLOv11n directly, with no architectural modification required.
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
6

## Slide 7
3. RESULTS — EXPERIMENTAL SETUP
Three Nano Models, Two Strategies
YOLOv5n, YOLOv8n, and YOLOv11n — three successive nano-scale generations of the YOLO family — were each trained under both a resized baseline and the proposed tiled strategy, for a controlled, model-agnostic comparison.
TRAINING CONFIGURATION
Framework
Ultralytics v8.3.213
Epochs
50
Input resolution
640 × 640 px
Augmentation
Mosaic, HSV, flips, scale
Optimizer
Auto (SGD / AdamW)
GPU
NVIDIA RTX 3050 Laptop (6GB)
WHY NANO MODELS?
Match the lightweight objective of routine laboratory deployment
Feasible on consumer-grade hardware without specialised imaging setups
Test whether resolution preservation — not model scaling — drives accuracy
Larger YOLO variants were deliberately excluded from evaluation
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
7

## Slide 8
3. RESULTS — DETECTION ACCURACY
Tiling Transforms Detection Accuracy
Chart: mAP@0.5 — resized vs. tiled inference (Table 2)
| YOLOv5n | YOLOv8n | YOLOv11n
Resized — mAP@0.5 | 0.449 | 0.613 | 0.663
Tiled — mAP@0.5 | 0.954 | 0.968 | 0.969
THE HEADLINE RESULT
44.9–66.3% → 95.4–96.9%
mAP@0.5 range across all three models, resized vs. tiled
+100%+
improvement in mAP@0.5:0.95 (stricter localisation metric)
The gain comes from preserving native resolution during inference — not from a bigger or newer model.
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
8

## Slide 9
3. RESULTS — COMPUTATIONAL COST
A Worthwhile Trade-Off
Tiling multiplies training time roughly fourfold — expected, since the tiled dataset has ~25× more samples — but whole-plate inference stays firmly practical for routine lab use.
Model
Train (resized)
Train (tiled)
Infer (resized)
Infer (tiled)
YOLOv5n
~1h 15min
~4h 50min
42 ms
285 ms
YOLOv8n
~1h 20min
~5h 10min
58 ms
298 ms
YOLOv11n
~1h 10min
~4h 45min
62 ms
312 ms
Whole-plate inference stays under 320 ms on a laptop RTX 3050 GPU — no TensorRT or quantisation required.
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
9

## Slide 10
3. RESULTS — TRAINING DYNAMICS
YOLOv11n: Steady Gains Over 50 Epochs
Chart: Validation metrics over training (Fig. 2)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
Precision (P) | 0.35 | 0.75 | 0.85 | 0.89 | 0.9 | 0.91 | 0.91 | 0.92 | 0.92 | 0.93 | 0.93
Recall (R) | 0.3 | 0.78 | 0.87 | 0.9 | 0.91 | 0.92 | 0.93 | 0.93 | 0.94 | 0.94 | 0.94
mAP@0.5 | 0.25 | 0.8 | 0.89 | 0.92 | 0.94 | 0.95 | 0.95 | 0.96 | 0.96 | 0.97 | 0.97
mAP@0.5:0.95 | 0.18 | 0.38 | 0.45 | 0.49 | 0.52 | 0.53 | 0.55 | 0.56 | 0.57 | 0.58 | 0.582
READING THE CURVES
0.21 → 0.582
mAP@0.5:0.95 rises steadily with no plateau — more epochs or mild augmentation could push it further
Precision ≈ Recall
by epoch 50 (≈0.93/0.94) — a well-balanced detector with few false positives or missed colonies
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
10

## Slide 11
3. RESULTS — CLASSIFICATION RELIABILITY
Consistent Separation Across 24 Species
23 / 24
Bacterial classes reaching
≥ 0.95 diagonal accuracy
< 0.01
Typical inter-class
confusion rate
0.16
Highest background
false-positive rate
(Streptococcus agalactiae)
The normalised confusion matrix (Fig. 3) shows the proposed tiled YOLOv11n model reliably distinguishes morphologically similar veterinary pathogens under varying imaging conditions. Diagonal values exceed 0.95 in 23 of 24 classes; nearly all inter-class confusions remain below 0.01. The only notable off-diagonal activity is between a few classes and the background — not between bacterial species themselves, which is the harder and more clinically important distinction.
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
11

## Slide 12
3. RESULTS — QUALITATIVE COMPARISON
Missed Colonies, Recovered
On a high-density blood agar plate with 26 closely packed colonies (Fig. 4), resize-based inference lost fine spatial detail — tiled inference recovered it completely.
RESIZED (640×640)
YOLOv8n-resized: misses 1 colony, 5 misclassifications
YOLOv11n-resized: misses 2 colonies, 3 misclassifications
Fine spatial detail lost during downsampling
TILED (20% overlap + NMS)
YOLOv8n-tiled: zero missed detections
YOLOv11n-tiled: zero missed detections
Only 1 duplicate false positive per model at tile borders
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
12

## Slide 13
3. RESULTS — SOTA COMPARISON & ROBUSTNESS
Small Model, Best-in-Class Accuracy
Chart: mAP@0.5 vs. published detectors (Table 4)
| ResNet-50 | MobileNetV2 | AlexNet | Faster R-CNN+HRNet | Cascade R-CNN+HRNet | ViT-L/16 | EfficientNetB6 | Original YOLOv8 | Proposed YOLOv11n
mAP@0.5 | 0.76 | 0.82 | 0.61 | 0.882 | 0.891 | 0.896 | 0.91 | 0.913 | 0.969
Proposed YOLOv11n reaches 0.969 mAP@0.5 with only 2.6M parameters — versus 27–304M in earlier heavy two-stage or transformer methods.
OVERLAP-RATIO SENSITIVITY
10% → 25% overlap changes mAP@0.5:0.95 by only 0.002 — 20% was chosen as the balanced setting.
5-FOLD CROSS-VALIDATION
0.967 ± 0.004
tiled mAP@0.5, vs. 0.663 ± 0.009 resized — stable across every fold
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
13

## Slide 14
4. CONCLUSION
Resolution Preservation Over Model Scaling
A simple tiled-inference pipeline with 20% overlap eliminates the resolution loss that cripples lightweight YOLO models on high-density Petri dish images — reaching 96.9% mAP@0.5 and 58.2% mAP@0.5:0.95 with YOLOv11n's 2.6M parameters, and under 320 ms whole-plate inference on a laptop GPU.
Resolution-preserving
Lightweight
Model-agnostic
Reproducible
Real-time
Sercan Külcü & Duygu Balpetek Külcü · Giresun University
sercan.kulcu@giresun.edu.tr
Overcoming Resolution Constraints in Automated Colony Counting via SAHI
14

## Slide 15
Thank You
Questions & Discussion
Sercan Külcü & Duygu Balpetek Külcü · Giresun University
sercan.kulcu@giresun.edu.tr