## Slide 1
RESEARCH ARTICLE · TURKISH JOURNAL OF MARITIME AND MARINE SCIENCES
Radar Image-Based Object Detection
and Tracking for Autonomous Surface Vehicles
A modular, lightweight HSV-segmentation and motion-aware tracking framework for real-time maritime situational awareness
Sercan KÜLCÜ
Giresun University, Faculty of Engineering, Computer Engineering, Giresun, Türkiye
Volume 12 · Issue 1 (2026) 35-47 | DOI: 10.52998/trjmms.1743670

## Slide 2
OVERVIEW
The Study at a Glance
A modular, real-time framework detects and tracks navigational targets on commercial marine radar screens, using colour-space segmentation for detection and a motion-aware identity strategy for tracking — evaluated on 7,200 real radar frames.
98.7%
True positive
detection rate
-59%
False positive
rate reduction
-75%
ID switches vs.
baseline tracker
240 ms
Average processing
time per frame
KEYWORDS
Autonomous surface vehicles
Radar image processing
HSV colour-space segmentation
Multi-target tracking
Computer vision
Embedded systems
Radar Image-Based Object Detection & Tracking for ASVs
2

## Slide 3
1. INTRODUCTION
Why Radar-Based Perception Matters
Autonomous surface vehicles (ASVs) need reliable, real-time detection of surrounding targets. Radar remains essential where optical sensors fail — in low light, fog, or storms — but radar imagery brings its own challenges.
⚠
Low resolution & noise
Radar frames show substantial noise and lower resolution than optical images, distorting target shapes.
⇆
Fluctuating echo area
Reflections vary with ship orientation, movement, and distance, so static area thresholds often fail.
▦
Fragile identities
Occlusion and sudden manoeuvres cause tracked objects to lose or swap their assigned IDs.
Radar Image-Based Object Detection & Tracking for ASVs
3

## Slide 4
1. INTRODUCTION
Two Limitations, One Framework
Existing systems typically rely on rigid area-based filtering and fragile ID management. This study addresses both limitations directly.
1
Orientation-aware area filtering
Targets are validated not only by instantaneous pixel area but by consistency with their prior trajectory and heading — preserving objects with temporarily distorted reflections.
2
Motion-predictive ID recovery
Lost targets are kept in an inactive buffer; if a new detection matches the predicted position and trajectory, the original ID is reassigned instead of creating a new one.
Radar Image-Based Object Detection & Tracking for ASVs
4

## Slide 5
2. MATERIALS & METHODS
System Pipeline Overview
▣
Capture
1200×1024 px
radar frame
→
⚛
Preprocess
Gaussian smoothing +
morphological filtering
→
◉
Detect
HSV segmentation +
orientation-aware filtering
→
⌖
Track
Euclidean matching +
trajectory-aware ID recovery
Built in Python with OpenCV and NumPy — lightweight enough for real-time embedded deployment, no GPU required.
Radar Image-Based Object Detection & Tracking for ASVs
5

## Slide 6
2.2 HSV-BASED DETECTION
Finding Targets by Colour
Commercial marine radar displays encode targets in yellow tones, with the own-ship marker in white. Converting each frame to HSV separates colour (hue) from brightness (value), making detection robust to lighting changes.
Threshold yellow hues within configurable HSV bounds to isolate navigational targets
Morphological open/close operations remove noise and bridge small gaps
Spatial moments (Eq. 1–3) yield each contour’s centroid and area
Only contours within a valid area range are kept — unless their centroid still matches the predicted trajectory
TARGET vs. OWN-SHIP ENCODING
Navigational targets
HSV ∈ [10–40]° hue, high sat/val (yellow)
Own-ship marker
Narrow white range: high value, low saturation
Radar Image-Based Object Detection & Tracking for ASVs
6

## Slide 7
2.3 DYNAMIC TARGET ASSOCIATION
Keeping Track of Every Target
Each frame's detections are matched to active tracks by Euclidean distance (Eq. 4). Unmatched detections start new tracks; targets missing for too long move to an inactive buffer rather than disappearing outright.
New Detection
→
Distance <
threshold?
→
Update Track
(reset age)
→
Age >
max_lost?
→
Recycle ID or
assign new
Why it works: a frame-indexed deque of recent centroids lets the system distinguish newly appearing objects from re-identifiable ones, while combining spatial proximity with trajectory similarity reduces false reassignments in high-density scenes.
Radar Image-Based Object Detection & Tracking for ASVs
7

## Slide 8
2.4 RELATIVE VELOCITY ESTIMATION
Is a Target Approaching or Receding?
Knowing raw position is not enough — an ASV needs to know how targets move relative to itself. The system compares each target's displacement to the own ship's own motion.
Target velocity
v = Δposition / Δt
Computed from centroid history in a deque buffer
Relative velocity
v_rel = v_target − v_ship
Subtracts the ship's own motion (Eq. 6–7)
Smoothing
ṽ_t = α·v_t + (1−α)·ṽ_{t-1}
Exponential filter stabilises noisy speed readings (Eq. 8)
This distinction — approaching, receding, or holding distance — gives more meaningful situational awareness than absolute motion alone.
Radar Image-Based Object Detection & Tracking for ASVs
8

## Slide 9
3.1 EXPERIMENTAL SETUP
Data, Configuration, and Ground Truth
DATA SOURCE
2 hours of screen recording from a Wartsilla ntpro 5000® Bridge Simulator (BridgeMaster radar), Fatsa Faculty of Marine Sciences, Ordu University.
1200×1024 px
Frame resolution
7,200
Radar frames evaluated
labelImg
Ground-truth annotation
KEY CONFIGURATION PARAMETERS
target_hsv_min / max
[10,50,50] – [40,255,255]
target_area_min / max
32 – 196 px²
distance_threshold
10 px
max_lost_frames
5
speed_multiplier
23.47 kts·s/px
Radar Image-Based Object Detection & Tracking for ASVs
9

## Slide 10
3.2 RESULTS — DETECTION ACCURACY
Orientation-Aware Filtering Improves Detection
Chart: Detection performance comparison
| Area-based only | Proposed method
True positive rate (%) | 94.5 | 98.7
False positive rate (%) | 2.7 | 1.1
READING THE RESULT
+4.4 pts
true positive rate over the area-based baseline
−59%
reduction in false positive rate (2.7% → 1.1%)
Combining area with heading/orientation cues lets the system tell real targets apart from noise and clutter far more reliably.
Radar Image-Based Object Detection & Tracking for ASVs
10

## Slide 11
3.3 RESULTS — TRACKING CONSISTENCY
Fewer Lost Identities, Longer Continuity
Chart: ID switch and total-ID comparison
| Baseline (positional only) | Proposed method
ID switch count | 112 | 28
Total generated IDs | 99 | 42
WHY IDENTITIES BREAK
ID switches typically happen when an object is briefly lost and recovered with a new ID — often after abrupt trajectory changes or close interaction with other targets.
By integrating motion features — speed and direction — into the ID-recovery logic, the proposed method preserves consistent trajectories over extended periods, even under occlusion.
Radar Image-Based Object Detection & Tracking for ASVs
11

## Slide 12
3.5 RESULTS — REAL-TIME PERFORMANCE
Efficient Enough for Embedded Deployment
⏱
240 ± 17 ms
Average latency
per frame
↻
~4 FPS
Sufficient for a 360°
scan every 2–3 s
⚙
10.6% ± 2.08
Average CPU usage
(peak 15.7%)
☷
111.2 ± 1.9 MB
Average memory
usage
Achieved on standard desktop hardware without GPU acceleration — a key requirement for resource-constrained, embedded ASV platforms.
Radar Image-Based Object Detection & Tracking for ASVs
12

## Slide 13
4. DISCUSSION
Strengths and Limitations
STRENGTHS
High detection accuracy (98.7% TPR) and strong tracking continuity (75% fewer ID switches)
Lightweight and interpretable — no training data or GPU required
Modular design supports sensor fusion and different radar colour encodings
Real-time capable on standard embedded hardware
LIMITATIONS & FUTURE WORK
Relies on manually tuned HSV thresholds and fixed area constraints
Overlapping targets can still occasionally cause ID swaps
Future: adaptive thresholding (histogram-based, k-means, ML-driven)
Future: multi-modal sensor fusion and validation on new radar data
Radar Image-Based Object Detection & Tracking for ASVs
13

## Slide 14
5. CONCLUSION
A Practical Framework for Maritime Perception
By integrating HSV colour segmentation, orientation-aware filtering, and motion-predicted ID reassignment, this framework achieves a 98.7% true positive detection rate across 7,200 radar frames, with an average processing latency of 240 milliseconds — demonstrating clear suitability for resource-constrained embedded systems and reliable real-time situational awareness in ASV navigation and surveillance.
Lightweight
Real-time
GPU-free
Modular
Extensible
Sercan KÜLCÜ · Giresun University
sercan.kulcu@giresun.edu.tr
Radar Image-Based Object Detection & Tracking for ASVs
14

## Slide 15
Thank You
Questions & Discussion
Sercan KÜLCÜ · Giresun University, Faculty of Engineering
sercan.kulcu@giresun.edu.tr